## Slide 1
NETWORK SECURITY & DATA INTEGRITY
Cyclic Redundancy Check (CRC) & Attendance File Auditor
Bitwise Polynomial Verification Dashboard | 3 Operating Modes | CSV File Tampering Detection
Pure Python XOR Engine
Zero external CRC libraries
Zero Bit-Flipping
Natural verification testing
Attendance Audit Case
Detects row deletion & edits

## Slide 2
BACKGROUND & CONTEXT
The Real-World Challenge: Attendance Record Integrity
⚠️ The Dilemma (Classroom Scenario)
• Instructor generates a CSV attendance file immediately after class.
• During storage, network transfer, or handling by intermediaries, values or rows may be altered or deleted.
• Manual line-by-line inspection is tedious, error-prone, and unscalable for large student cohorts.
• How can the instructor audit the file to determine whether it remains 100% identical to the original?
🛡️ The Solution: Cyclic Redundancy Check (CRC)
• Cryptographic-like mathematical fingerprint generated using bitwise polynomial modulo-2 division.
• Reference CRC: Computed on pristine original attendance file right after generation.
• Audited CRC: Computed on received file at any point during later storage or audit.
• Instant Verification: CRC match proves file authenticity; any bit mismatch immediately flags tampering!

## Slide 3
THEORETICAL FOUNDATION
Core Mechanics of Cyclic Redundancy Check (CRC)
1. Modulo-2 XOR Arithmetic
Binary Division Without Carries
• CRC uses binary modulo-2 arithmetic.
• Addition and subtraction are identical to bitwise XOR (^).
• 1 ^ 1 = 0, 0 ^ 0 = 0
• 1 ^ 0 = 1, 0 ^ 1 = 1
• Eliminates complex carries, making hardware and software execution ultrafast.
2. The Polynomial Formula
D(x) · 2^k + R(x) = C(x)
• Data bits D are padded with k zeros, where k = len(G) - 1.
• The padded stream is divided by Generator Polynomial G(x).
• The division remainder R(x) is the CRC checksum.
• Transmitted Codeword = Data + Remainder.
3. Receiver Verification
Remainder Check Condition
• Receiver receives the codeword and divides by the exact same G(x).
• If Remainder == 0:
-> No error detected! Codeword is authentic.
• If Remainder != 0:
-> Corrupted! Flag tampering immediately.

## Slide 4
SYSTEM CONFIGURATION
Supported CRC Standards & Generator Polynomials
CRC-3 (3 Bits Checksum)
Polynomial: x³ + x + 1 | Standard: Educational / Telemetry
Generator 'gen': 1011
Compact 3-bit checksum used for demonstrating polynomial division fundamentals.
CRC-4 (4 Bits Checksum)
Polynomial: x⁴ + x + 1 | Standard: ITU G.704 Framing
Generator 'gen': 10011
4-bit CRC standard widely used in digital telecommunications and framing systems.
CRC-8 (8 Bits Checksum)
Polynomial: x⁸ + x² + x + 1 | Standard: ATM / Sensor Protocols
Generator 'gen': 100000111
1-byte checksum delivering robust burst error detection for text and structured files.
CRC-32 (32 Bits Checksum)
Polynomial: IEEE 802.3 Standard | Standard: Ethernet / ZIP / PNG
Generator 'gen': 100000100110000010001110110110111
Industry-standard 32-bit polynomial detecting 99.9999999% of all transmission errors.

## Slide 5
OPERATING MODE 1
Mode 1: Binary Input & Codeword Verification
📤 Sender Side: Codeword Generation
Input: User provides raw binary string, e.g. 100100.
Zero Padding: Padded with k zeros: new_data = data + '0'*crc_len.
CRC Generation: Calculated using pure bitwise XOR: sender_crc = crc(new_data, gen).
Transmitted Codeword: Formed by appending CRC: codeword = data + sender_crc.
Example Output:
• Data: 100100 | Gen: 1101 (CRC-3)
• Sender CRC: 001
• Codeword: 100100001
📥 Receiver Side: Remainder Verification
Input: Receives binary codeword (manual entry or direct test).
Remainder Division: remainder = crc(received_codeword, gen).
Deterministic Error Check:
• If int(remainder, 2) == 0:
✔ Status: No Error Detected
Extracted Data: received_codeword[:-crc_len]
• If int(remainder, 2) != 0:
✖ Status: Error Detected (Data Corrupted)
Strict Policy: No artificial flipping! Receiver evaluates authentic input.

## Slide 6
OPERATING MODE 2
Mode 2: Text Input & CRC Value Comparison
🔤 Text to 8-Bit Binary Conversion: text_to_binary(text)
Converts every character into an 8-bit ASCII bitstream: ''.join(format(ord(char), '08b') for char in text). Enables arbitrary natural language strings to be mathematically processed by polynomial division.
✔ Case A: Identical Text (No Error)
• Sender Text: 'Computer Networks CRC Lab'
• Receiver Text: 'Computer Networks CRC Lab'
• Sender CRC: 00001000
• Receiver CRC: 00001000
• Verdict: Sender CRC == Receiver CRC
• Result: No Error Detected (Data authentic)
✖ Case B: Single Typo / Alteration
• Sender Text: 'Computer Networks CRC Lab'
• Receiver Text: 'Computer Networks CRC lab' (lowercase 'l')
• Sender CRC: 00001000
• Receiver CRC: 01001011
• Verdict: Sender CRC != Receiver CRC
• Result: Error Detected! 1-bit text shift creates completely different remainder.

## Slide 7
OPERATING MODE 3
Mode 3: File Input & Attendance CSV Audit
Test 1: Pristine Original Record
AUTHENTIC RECORD VERIFICATION
Original file compared against itself or uncorrupted copy.
Original CRC: 01111001 Audited CRC: 01111001
Verdict: PASS (No Error Detected)
Test 2: Attendance Status Tampered
DETECTING ACCIDENTAL MODIFICATION
Student 103 status changed from 'Absent' to 'Present'.
Original CRC: 01111001 Audited CRC: 11101000
Verdict: FAIL (Tampering Detected)
Test 3: Student Row Deleted
DETECTING ACCIDENTAL ROW REMOVAL
Student 105 row removed during transfer.
Original CRC: 01111001 Audited CRC: 10011110
Verdict: FAIL (Row Deletion Detected)
📊 Audit Trail & CSV Report Generation
Instructors can download timestamped verification reports (CSV) certifying file integrity for administrative compliance.

## Slide 8
CONCLUSION & HIGHLIGHTS
Architecture Summary & Key Takeaways
Strict Implementation Rules
• 100% Pure Python XOR Engine: Zero external CRC libraries (no zlib / hashlib).
• Strict adherence to provided crc() and text_to_binary() functions.
• No Bit-Flipping Controls: Evaluates natural user inputs and authentic files without synthetic flipping shortcuts.
Dashboard Features
• Dynamic CRC selection (CRC-3, CRC-4, CRC-8, CRC-32) + Custom generator input.
• Multi-mode switching: Binary Codeword, Text Comparison, and File Attendance Audit.
• Live tabular preview of CSV records & instant visual audit verdicts.
Key Educational Takeaways
• CRC provides mathematical certainty for detecting accidental transmission errors.
• Solves the instructor's classroom dilemma: audits files reliably without manual overhead.
• All 3 modes verified with automated unit tests (test_crc_rules.py).